## Slide 1: TrackView Pro & EMSuite 2026

## Slide 2: Monitoring System Structure Overview
TVP AP
TVP PoE
TVP RF
TVP RF-DC
Beacon/
Sounder
Cloud based
Middleware
On-Site or Remote
User PC interface
Mobile App
Email
Option 1:
Local Server
Option 2:
Cloud Server
Microsoft
Azure
HTTPS
HTTPS
SMS
Voice
Ellab Connect
PoE or Ethernet
Aerial
Aerial
Via Digital Output Sensor
Via Digital Output Sensor
Via
Soft PLC
Notes: This diagram shows how all the components can connect into one software platform and shows all options for data collection.
The system allows all our wireless hardware to be used together.
Users can view data in the following ways:
On a local PC
On any PC with internet access
On a tablet
On a mobile device
Via the alarm App
Alarms by email, text (SMS), or Voice Call

## Slide 3: Full system overview
Protect valuable assets and comply with industry regulations

## Slide 4: Hardware Overview
Radio Frequency transmitter Power over Ethernet Transmitter Radio Frequency & DC Transmitter Access Point

## Slide 5: TrackView Pro Hardware
Access Point
Radio frequency
LoRa; Long Range
- Wireless communication and low power consumption
Communicates with up to 32 RF Transmitters
Operates in -20˚C to +60˚C
Operates in 0 to 90% humidity
Requires:
Ethernet cable
Power source (a part of purchase)
USB cable (FW upgrade)
Back up battery (2-3h) Charges during direct power supply
Relay outputs:
Beacons (sound)
Flashing lights
RF 868MHz
EU, UK, Switzerland & United Arab Emirates
RF 920 MHz
Japan, Malaysia & Singapore
RF 915MHz
USA & Canada
RF 915-928MHz
Australia, New Zealand & Brazil

## Slide 6: Access Point
Display Information
Ethernet communication status
Active transmitters
Transmitter battery level
Ethernet communication status
(Blinking blue if no ethernet, green if connected, red in alarm)
Buzzer disabler/ Page scroller
Alarm relay status
Transmitter signal strength
Local power outlet
Ethernet port for communication with server and Power over Ethernet transmitter(PoE)
USB Port
Alarm relays (x2) Max Relay Voltage & Current: 24DC/ 1A

## Slide 7: Access Point
Alarm Relay
Power/LAN Relay (example: to control light)
USB Connector
Ethernet Connector / PoE
12V DC Jack Connector / Power Supply
1.
2.
3.
4.
5.
Only use the power supply provided by Ellab.

## Slide 8: Access Point
Back lid & Battery connection
Back lid
Rechargeable
battery pack
Battery pack
connection

## Slide 9: TrackView Pro Hardware
Transmitter
Operates in -20˚C to +60˚C
RF 868MHz
EU, UK, Switzerland & United Arab Emirates
RF 920MHz
Japan, Malaysia & Singapore
RF 915MHz
USA & Canada
RF 915-928MHz
Australia, New Zealand & Brazil
Data integrity
Backfilled data
Hardware output
RF Transmitters – radio frequency;
One year battery life; One temperature sensor
Energizer Ultimate Lithium battery
PoE Transmitters – Power over Ethernet;
Few days (back up) battery; if disconnected to Ethernet
Sample rate 1 second
Transmit rate 2 minutes
Log rate 10 second
Communication and power via cable

## Slide 10: TrackView Pro PoE Transmitter
Live feed with super-fast transmission rate
  Quick update
Battery consumption is not a concern due to PoE cable
Access Point (Rx) not required
2x AA batteries back up if PoE failure
24V DC power output (for powering custom sensors)
More costly for initial setup:
  Ethernet connection required
More costly to relocate
Key Benefits
Main Restrictions

## Slide 11: TrackView Pro Transmitter
Back Lid & Battery connection
Back lid
Increased transmission rate & data pts will reduce batteries lifetime
USB Connection (Firmware update)
Batteries (x2) Recommend Lithium, long lasting particularly at lower temperatures
Screw or magnet
locations

## Slide 12: TrackView Pro Transmitter
Latch in locked position
Latch in unlocked position
Notched SMART connector
Transmitter
Back plate
Hidden latch
Notched SMART connector

## Slide 13: Transmitter
Display Information
Detachable SMART sensor
Alarm Status LED
Blinks red when alarm activated
Live measurement values
Signal strength to access point
Battery level indicator
Buzzer disabler/ Page scroller
Communication status with access point
Alarm status indicator (channel specific) Configured via EMSuite Software
Buzzer dis/enabled from EMSuite

## Slide 14: Transmitter
Default transmit rate: 10 minutes
Default sample rate: 2 minutes
Configurable in the software
Transmit interval to TVP Access Point overridden when an alarm is triggered
Alarm originates from the transmitter
RF / DC transmitter
Default transmit rate: 10 second
Default sample rate: 1 second
Default Log rate: 10 second
Configurable in the software
PoE transmitter
Transmit; data send to EMSuite
Sample; triggers alarm
Log; data stored

## Slide 15: Sample vs. Log vs. Transmit Rates
Sample Rate: How frequently a sample is taken
Log Rate: How frequently the data is stored in the transmitter for backup if connection is not available
Transmit Rate: How frequently is data sent to the software
RF Transmitter
Sample Rates:
Min: 1 minute
Max: 2 hours
Log Rates:
Equal to Sample Rate
Transmit Rates:
2x to 5x the Sample Rate
  5x is recommended
PoE Transmitter
Sample Rates:
Min: 1 second
Max: 2 hours
Log Rates:
1x to 10x the sample rate
Transmit Rates:
10x the Sample Rate
  min of 10 seconds

## Slide 16: One year battery life
Sample & Transmit rate
The table shows required setup for one year battery life
Theoretical calculation for the wireless RF transmitter
One temperature sensor with 1 minute sample rate & 5 minutes transmit rate – One year battery life

## Slide 17: Hardware communication
Tx radio module is activated only for the duration of the 2-way communication
Handshake ensures reliable data and error-free data exchange; achieving FDA 21 CFR Part 11 compliance
Handshake
Secures correct data with two-way communication
Communicates 100meters indoors
Secure Internet Protocol
URL required for configuration
No need of static IP address (DHCP)
Auto-Discovery
Transmitter; broadcast message to (nearby) AP
Hardware displayed in EMSuite – easy to implement
Data from Transmitter to AP
Data stored in Transmitter and Access Point
Data stored in transmitter is removed after the handshake (both from AP & EMSuite)
Radio Link
Handshake
EMSuite
Rx radio module is always activated

## Slide 18: TrackView Pro Transmitter
Transmitter 484899
Smart Sensor 122233
Smart Sensor 122234
Channel 484899-1
Channel 484899-2
Channel 484899-6
Channel 484899-5
Each transmitter may host up to 2 smart sensors
Each smart sensor contains 1-2 sensor channels
Hot Swapping Smart sensors
Versatile measurement types
Example:
If you use our integrated smart sensor, with temperature(T) and humidity(RH), then you have used 2 channels. One channel for temperature and one channel for humidity.
Notes: The smart sensor can each hold from 1-4 channels. A smart sensor can be replaced by another smart sensor by hot swapping. The new smart sensor may contain channels of the same type as the replaced smart sensor, or of a different measurement type.
When replacing a smart sensor with a sensor with channels of the same measurement types, measurements will continue as the same data series.
Replacing a smart sensor with a sensor with channels of different measurement types requires that the user decommission the channels on the replaced smart sensor. There will be a discontinuation between old and new data series, and decommissioned data is not shown on graphs. Decommissioned data may be accessed through reports.
18

## Slide 19: TrackView Pro Transmitter
Hot Swapping Smart sensors
Same Measurement Type
Continuous data session
If “plugged-in” sensor not authorised on another transmitter
  No user action required
  Change registered in Audit Trail
Different Measurement Type
Dicommisson of channel
Decommissioning removes channels from:
  Sites and zones
  Logical zones
  Reports
  Scheduled reports
  Alarm templates
  Active alarms
Notes: The smart sensor can each hold from 1-4 channels. A smart sensor can be replaced by another smart sensor by hot swapping. The new smart sensor may contain channels of the same type as the replaced smart sensor, or of a different measurement type.
When replacing a smart sensor with a sensor with channels of the same measurement types, measurements will continue as the same data series.
Replacing a smart sensor with a sensor with channels of different measurement types requires that the user decommission the channels on the replaced smart sensor. There will be a discontinuation between old and new data series, and decommissioned data is not shown on graphs. Decommissioned data may be accessed through reports.
19

## Slide 20: Channels and Datapoints
Datapoints stored in transmitter
Stored data serves as back-up ; backfilled into EMSuite
Smart Sensor provides data into EMSuite; Disconnected sensor stops the recording of data
Example: Backfill time 2,2 hours for 24 hours memory
ETSI (European Telecommunication Standard Institute) standards: Limited transmit duty cycle of 1% (36 seconds per hour) which reduces the backfill capability
Data retained in the transmitter depends of the number of days the communication is lost, and the transmit interval and numbers of attached sensors.
If PoE; we can backfill UP TO 10 data packets per transmit If RF; we can backfill UP TO 11 data packets per transmit.

## Slide 21: TrackView data memory – RF transmitter
How many days can the transmitter be without communication without losing data?
From EMSuite version 1.5.2+
Sample rate (minutes) | Transmit rate (minutes) | Number of sensors | Days | Number of samples
1 | 1 | 1 | 14 | 20.750
1 | 5 | 2 | 37 | 59.300
1 | 5 | 1 | 54 | 77.840

## Slide 22: Hardware Overview
Sensors - Transmitter – Access Point
3rd
Option 2)
±1250PA
Option 1)
±100PA
Rotronic
Ellab RH/T
-20 to 60C
-200 to 250C
Vaisala GMP 251 sensor
PoE Unit
Required
4-20mA
0-10V
Digital in- & output
Analog
Transmitter Access Point

## Slide 23: Terminology
TVP: TrackView Pro
Tx: Transmitter
Transmitter “can” also be called a logger or data logger or device
Rx: Receiver
Ellab’s Receiver is called TrackView Pro Access Point or TrackView Pro Network Access Point
AP: Access Point
RF: Radio Frequency
PoE: Power over Ethernet
S/W: Software
H/W: Hardware
WP: Waterproof
dP: Differential Pressure
T: Temperature
RH: Relative Humidity
CO2: Carbon Dioxide
Sensor can be measuring T, T/RH, dP, CO2
Sensor is also called a probe or a sensor probe
A measurement point is an individual parameter
e.g. T/RH counts as 2 measurement points

## Slide 24: Temperature sensors
PT1000
Ellab Smart sensor PT1000 | 
Temperature: | -200C to +200C
Cable options: | 3- and 5- meter length
Cable diameter: | 3mm
Sensor: | 71mm x ø4mm Waterproof
Additional info: | See datasheets
Ellab Smart sensor PT1000, thin wire | 
Temperature: | -200C to +200C
Cable options: | 3- and 5- meter length
Cable diameter: | 2mm
Sensor: | 70mm x ø3mm Waterproof
Additional info: | See datasheets

## Slide 25: Integrated smart sensors – Temperature
Ellab Smart sensor PT1000 with integrated T | 
Temperature: | -20C to +60C
Cable options: | N/A
Cable diameter: | N/A
Sensor: | Integrated 2.5mm
Additional info: | See datasheets
Calibration: | 40 cm roll out cable for dryblock

## Slide 26: Integrated smart sensors – RH/Temp
Ellab Smart sensor with integrated T/RH | 
Temperature: | 0C to +40C
Humidity: | 0-100%
Cable diameter: | N/A
Sensor: | Integrated
Additional info: | See datasheets

## Slide 27: RH/Temperature - Rotronic HygroClip2
Ellab Smart sensor with Rotronic HygroClip2 integrated T/RH | 
Temperature: | -50C to +100C
Humidity | 0-100%
Cable options: | 2- and 5- meter length or none
Smart connector: | Mandatory
Additional info: | See datasheets
Attention:
- Cable options: 2 and 5 meters, ordered separately
- Can be used without cable
- Smart connector, ordered separately

## Slide 28: NEW! RH/Temperature – TVP RH/T Pro Smart Works from 1.5.2
Ellab Smart sensor with integrated T/RH | 
Temperature: | -50C to +60C
Humidity | 5-95%
Cable options: | 2, 3- and 5-meter length or none
Smart connector: | Mandatory
Additional info: | See datasheets

## Slide 29: Door Sensors – Light, Medium & Heavy
Ellab Smart sensor with door contact | 
Operating temperature: | -20C to +60C
Cable options: | 3 meter
Cable diameter: | N/A
Sensor: | Door contact
Additional info: | See datasheets
Ellab Smart sensor with door contact | 
Operating temperature: | -20C to +60C
Cable options: | 3 meter
Cable diameter: | N/A
Sensor: | Door contact
Additional info: | See datasheets
Ellab Smart sensor with door contact | 
Operating temperature: | -20C to +60C
Cable options: | 3 meter
Cable diameter: | N/A
Sensor: | Door contact
Additional info: | See datasheets

## Slide 30: Door sensor

## Slide 31: Differential pressure (DP)
Ellab Smart sensor with Differential Pressure(DP) | 
Operating temperature: | -20C to +60C
Measuring range: | +-100Pa
Resolution: | +-0.1Pa
Pressure connector: | DP V1: LEMO air for ø6mm tube DP V2: Barb Fittings for ø6mm
Additional info: | See datasheets
Ellab Smart sensor with Differential Pressure(DP) | 
Operating temperature: | -20C to +60C
Measuring range: | +-1250Pa
Resolution: | +-1.0Pa
Pressure connector: | DP V1: LEMO air for ø6mm tube DP V2: Barb Fittings for ø6mm
Additional info: | See datasheets
New design!
Smaller size
Works from EMSuite V1.5.3+

## Slide 32: Smart sensors with analog input
Ellab Smart Sensor - Analog Input 4-20mA | 
Operating temperature: | -20C to +60C
Input range: | 4-20mA
Measure accuracy: | +-20µA
Output power: | Max 1W
Additional info: | See datasheets
Ellab Smart Sensor - Analog Input 0-10V | 
Operating temperature: | -20C to +60C
Input range: | 0-10V
Measure accuracy: | +-10mV
Output power: | Max 1W
Additional info: | See datasheets
Comes in two variations:

## Slide 33: Smart sensors with digital in- & output
Ellab Smart sensor with Digital Input | 
Temperature: | -20C to +60C
Drive: | From customer relay
Communication interface: | Ellab Smart USB
Usage: | Signal from PLC, etc.
Additional info: | See datasheets
Ellab Smart sensor with Digital Output | 
Temperature: | -20C to +60C
Drive: | Galvanic Solid State Relay
Communication interface: | Ellab Smart USB
Usage: | Light & sound beacon
Additional info: | See datasheets
Comes in two variations:

## Slide 34: Airflow Sensor – E+E
Ellab Smart Sensor with Air Flow | 
Operating airflow range | 0-5, 0-10 and 0-20 m/s
Operating temperature range | -20C to +60C
Cable length | 2-meters
Communication Interface | 0-10V
Requires power supply
*Available with and without Power Supply

## Slide 35: Light towers & beacons
For alarm notifications
Alarm Beacon without sound | 
Operating temperature | -20˚C to 40˚C
Light | Red flashing light
Sound | N/A
Communication Interface | Ellab Digital Output
Alarm Beacon with sound | 
Operating temperature | -20˚C to 55˚C
Light | Red flashing light
Sound | Yes
Communication Interface | Ellab Digital Output
Ligth Towers for cleanroom | 
Operating temperature | -10˚C to 50˚C
Light | Yes - customizable
Sound | Yes – customizable
Communication Interface | Ethernet

## Slide 36: Digital Output
Transmitter connected with a Beacon
Activated with Ellab Smart sensor – Digital output
Enabled by clicking “Hardware Output” in alarm settings – Threshold

## Slide 37: Application overview
What type of applications can we monitor?
Refrigerators/Cold Rooms
Reach-ins & Walk-ins
LN2 Freezer/ Cryogenic Tanks
Stability/environmental chambers
Incubators
Laboratories
Warehouse & storage areas
Clean rooms
Water Baths

## Slide 38: TrackView Pro Hardware – Smart Sensor Options
3rd
PoE Unit
Required
PT1000 sensor
Ellab T/RH sensor
Rotronic HC2 T/RH sensor
Vaisala GMP 251 sensor
4-20mA
0-10V
Differential Pressure sensor
Door Open/Close sensor
Radio Frequency transmitter Power over Ethernet Transmitter Radio Frequency & DC Transmitter Access Point
Transmitter options
Notes: 3rd party sensors need to be independently powered. We are reading the data their sensor provides for an output.

## Slide 39: LN2 Freezers / Cryogenic Freezers
Temperature: 4mm Probe, 3mm Cable
Temperature: 3mm Probe, 2mm Cable
Temperature
Common Conditions:
-196C to -135C
Notes: Don’t forget to add on the LN2 calibration

## Slide 40: Reach-ins & Walk-ins
Temperature: 4mm Probe, 3mm Cable
Temperature: 3mm Probe, 2mm Cable
Temperature
Common Conditions:
-150C to -20C
2 to 8C
Notes: Don’t forget to add on the LN2 calibration if going below -85C

## Slide 41: Stability & Environmental chambers
Temperature: 4mm Probe, 3mm Cable
Temperature: 3mm Probe, 2mm Cable
Temperature
Relative Humidity
Rotronic HC2
Common Conditions:
25C/60%RH, 30C/65%RH
30C/75%RH, 40C/75%RH

## Slide 42: Incubators
Carbon Dioxide
Vaisala
GMP251
Temperature: 4mm Probe, 3mm Cable
Temperature: 3mm Probe, 2mm Cable
Temperature
Relative Humidity
Rotronic HC2
Common Conditions:
37C, 37C/>90%RH, 37C/>90%RH/5%CO2
37C/>90%RH/10%CO2
55C

## Slide 43: Labs, Storage Areas, Warehouses
Ellab, ambient sensor with removable cap for calibration
Temperature
Relative Humidity
Ellab RH/T Smart sensor
Common Conditions:
15~30C
20~25C
Ambient RH

## Slide 44: Clean Rooms – Core Functionality
Direct Connect with removable cap for calibration
Temperature
Relative Humidity
Differential Pressure
Direct Connect
Individually placed or grouped in encasement
Common Conditions:
15~30C
20~25C
Ambient RH
Notes: Light towers can be provided through Ellab
Particle counters are sourced separately. Must have Modbus TCP-IP

## Slide 45: Clean Rooms – Advanced Functionality
Light Towers
Light Tower:
Patlite
LA6-5DSNWB-POE
Modbus TCP-IP Capable
Customer Sourced
Particle Counters
Airflow
3rd Party Airflow Sensors
Notes: Light towers can be provided through Ellab
Particle counters are sourced separately. Must have Modbus TCP-IP

## Slide 46: Particle counter enabled within EMSuite
ModBus TCP connection with Ellab Connect
Manufacturer | Works with EMSuite 1.5.0
Climet Cleanroom Particle Counters - Climet | Yes
Lighthouse Airborne Particle Counters Archives - Lighthouse Worldwide Solutions | Yes
Beckman Coulter: Met-One Air Particle Counters | Yes

## Slide 47: Water Baths / Bead Baths
Common Conditions:
37C, 42C, 55C
Temperature: 4mm Probe, 3mm Cable
Temperature: 3mm Probe, 2mm Cable
Temperature

## Slide 48: Applications with TrackView Pro
What can a customer measure within our monitoring solution?

## Slide 49: TrackView Pro Analog 4-20mA & 0-10V wiring example
External
+ Power -
Supply
External
+ Power -
Supply
4-20mA
0-10V
RF transmitter
4-20mA
0-10V
PoE transmitter
24 VDC power from the PoE

## Slide 50: Range Test Kit
A Signal strength of minimum 60% ensures good communication
The TrackView Pro – Range tester contains:
- One Access Point
- One transmitter
- One-pager instructions

## Slide 51: Demonstration Kit
Transportation case with Laptop and EMSuite installed
1x Access Point
1x Transmitter (Radio Frequency)
1x Ellab RH/T integrated sensor
1x Ellab PT1000 temperature sensor -200˚C to +250˚C (3 meter)
1x Laptop w. Power supply
1x Master USB
Mounting Bracket for Access Point
Mounting Bracket for RF transmitter
Suitcase with wheels

## Slide 52
What and how is this used?
EMSuite

## Slide 53: What is EMSuite?
Overview
Site, Zones and channels
Data collection
Collected in EMSuite
Alarms
Audit trails
Reports

## Slide 54: EMSuite – Navigation pane
Personalised View by/ for individual users
Create & Manage Sites/ Zones & Allocate Channels
Customisable Reports
Brings channels from multiple areas
Locations, parameters, history & ackt
Audit time, category, users, actions, activities
Manual calibration & Verification
Create/ Edit Map & View of Floorplans
Alarm Settings, Users and Roles, H/W, API…
Create and manage SoftPLC rules

## Slide 55: Control Center
Hardware
Auto Discovery
Hardware configuration
Checking serial number
Access point detects all nearby sensors; Auto discovery
Authorize

## Slide 56: Control Center
Channel Configuration
Edit channel name
Deactivate
Decomission

## Slide 57: Control Center
Transmitter
Sample & transmit rate
Name
Change Access Point for better signal strength
Request History to check communication

## Slide 58: Control Center
Access Point
Edit name
Edit description
Check transmitters connected

## Slide 59: Users & Roles
Add a User in EMSuite with dedicated permissions
Create User by defining log in credentials and Role definition
Enable Sites & Zones for the User
Add Role type to specific User

## Slide 60: Sites & Zones
Manage Sites in EMSuite
Create Site with initial Zone
Add Channels

## Slide 61: Creating Alarms
Alarm templates within EMSuite
4 threshold types
Operation mode defined in alarm settings
Notification; General or each threshold
Multiple measurement types for each template

## Slide 62: Create Action Card
Follow existing SOP’s to prevent wrongful Alarm Acknowledgements

## Slide 63: How to claim an Action Card
Go through the steps to ensure correct Alarm Acknowledgement

## Slide 64: Audit Trail
To ensure and keep track of entries and actions within EMSuite
  User administration
  System configuration
  Hardware
  Alarm

## Slide 65: Report
Manage reports within EMSuite
Report modules
Report folder in EMSuite saves created reports for 7 days
Schedule report – how?
CSV export & PDF file

## Slide 66: Map within EMSuite
Interactive Map to create overview of the site
Upload image in “Interactive Map”
Drag and drop – AP and sensors
Define site and zone from the dashboard

## Slide 67: Floor map

## Slide 68: Displaying Alarms on Map
Channel status within sites and zones

## Slide 69: Enable Operation Mode within EMSuite
Manage different modes to avoid unnecessary alarms
Enable Operation mode in System settings
Configured in Alarm settings
Activated in Soft PLC
Operation Mode Alarms ONLY active during “On” switch from Soft PLC

## Slide 70: Soft PLC
Software Programmable logic controller
Controls and supervises inputs

## Slide 71: Monitoring System Structure Overview
TVP AP
TVP PoE
TVP RF
Beacon/
Sounder
Cloud based
Middleware
On-Site or Remote
User PC interface
Mobile App
Email
Option 1:
Local Server
Option 2:
Cloud Server
Microsoft
Azure
HTTPS
HTTPS
SMS
Voice
Notes: This diagram shows how all the components can connect into one software platform and shows all options for data collection.
The system allows all our wireless hardware to be used together.
Users can view data in the following ways:
On a local PC
On any PC with internet access
On a tablet
On a mobile device
Via the alarm App
Alarms by email, text (SMS), or Voice Call

## Slide 72: Environmental Monitoring In Operations
Cost
  Ownership
  Maintenance
Security
  Network performance
  Backup
  Data recovery
Scalability
  Usage plan
Implementation
  Who does what?
Purchase
Purchase