## Slide 1
TrackSense® Wireless Data Loggers

## Slide 2: TrackSense® Data Logger System
Temperature
Your Life Science
Compliance
Partner
Measured Parameters
Pressure/Vacuum
Conductivity
Humidity
CO₂
Compact Design:
Industry-leading stability with stainless steel housing
Key Features
Sky Radio Technology
Wireless data transmission
Online start and stop
No data loss
Alarm functionality
Exceptional accuracy: ±0.05 °C
Interchangeable sensors
Measurement range from -196 to +400 °C
Notes: All those services if done by our teams or the customers teams, are supported by the best software on the market for thermal validation projects.
Easy setup and various installation options to meet the customers requirements.
Compliant to the global standards.
Quick results & fast evaluation as well as compatibility with 3rd party validation software like KNEAT.
A real time saver, as you can repeat studies easily or start them with out any setup. You also can work offline and at the same time do reports somewhere else with the dual dynamic installation.

## Slide 3: TrackSense® Data Logger Overview
Pro
Pro X
Pro XL
Lab
Compact
Frigo UX Sky
Frigo
Micro
Mini
-50 to +150 °C
-80 to +150 °C
-80 to +150 °C
-30 to +100 °C
-30 to +140°C
-90 to +140 °C
-90 to +85 °C
-20 to +140 °C
0 to +140 °C
Basic
-30 to +108 °C
Interchangeable sensor
Integrated sensor

## Slide 4: General Features (1/2)
Withstands -80 to +150 °C and up to 10 bar pressure (extended to -196 to +400 °C with thermal barrier)
Fast response time with thin probes (minimized thermal error)
Accuracy: ±0.05 °C / ±0.25% FS (0-8 bar) / ±2% RH
Replaceable battery (up to 1,000 operating hours)
Large non-erasable memory (up to 120,000 data points)

## Slide 5: General Features (2/2)
Durable and high-quality build:
Electronics sealed in protective plastic
High-end components
ISO-certified production
Extensive quality control—even for stocked items
Battery:
Specialized battery for up to 150 °C
Software warning for low capacity
Correct measuring position:
Extensive accessories and fixations
Custom sensor designs (length & diameter)

## Slide 6: Data Point Distribution
Sensor type | Data point distribution |  | 
 | When using 3. Gen. Pro Logger (120.000 Datenpunkte) |  | 
Temperature Single sensor | 120.000 points |  | 
Temperature Double sensor | 60.000 points per channel |  | 
Multipoint Temperature sensor | 30.000 points per channel |  | 
Quad Sensor | 30.000 points per channel |  | 
Thermocouple Sensor | 40.000 points | 80.000 for temp calculation | 
Pressure sensor | 60.000 points | 60.000 for temp compensation | 
Pressure- / Temperature sensor | 40.000 pressure | 40.000 temperature | 40.000for temp compensation
Vacuum-/Temperature sensor | 60.000 vacuum | 60.000 temperature | 
Humidity-/Temperature sensor | 60.000 humidity | 60.000 temperature | 
Conductivity-/Temperature sensor | 60.000 conductivity | 60.000 temperature | 
CO2 Sensor | 120.000 CO2 |  | 
Automarker Sensor | 120.000 |  | 

## Slide 7: Multi - Reader Station
Easy USB or LAN connection to PC
Up to 3 expansion readers (requires power supply)
Simultaneous programming, starting, and readout (up to 16 loggers)
Inductive data transfer

## Slide 8: Interchangeable Sensors
Choose between Temperature-, Pressure-, relative Humidity-,
CO2- and Conductivity sensors.

## Slide 9: Rigid and Combined Temperature Sensors
Rigid:
Stainless steel
-196 to +150 °C
Ø2 mm
1 or 2 channels
Combination (rigid/flexible):
Stainless steel/PTFE
-196 to +150 °C
Ø1.8–2 mm

## Slide 10: Flexible Temperature sensors
Smart flex. Single-/Double sensor
PTFE
-196 to +140 °C
Ø1.8 mm
Low temperature sensor
PTFE
-196 to +100 °C
Ø1.2 mm
Semi flex. Single-/Double sensor
Stainless steel
-196 to +150 °C
Ø1.5 mm
High temperature sensor
Stainless steel
0 to 400 °C
Ø2 mm

## Slide 11: Thermocouple Sensor
Replaceable probe tip using screwdriver
Temperature Range logger exposed: -50 to 62 °C
Temperature Range only thermocouple: -50 bis 400 °C
Accuracy: ±0.3 °C

## Slide 12: Pressure & Temperature Sensors
Pressure sensor
Pressure: 10 mBar to 4, 6 or 8 Bar abs, Accuracy: ±0.25% FS
Pressure-/Temperature sensor
Temperature: 0 to 150 °C, Accuracy: ±0.5 °C
Vacuum & Temperature Sensor
Pressure: 0.0001 to 1,000 mBar, Accuracy: ±15–20% depending on range
Pressure accuracy: 0,0005 mbar to 0,001 mbar: ±20 %
0,001 mbar to 100 mbar: ±15 %
100 mbar to 1.000 mbar: ±20 %

## Slide 13: Humidity & Temperature Sensor
Humidity: 0–100% RH, Accuracy: ±0.2%
Temperature: 0–90 °C, Accuracy: ±0.1 °C

## Slide 14: Conductivity & Temperature
Variant 1:
0–200 µS/cm
Temp Range: 0–100 °C
Variant 2:
200–2000 µS/cm
Temp Range: 0–100 °C

## Slide 15: CO2 Sensor & Automarker Sensor
Automarker-Sensor
Logs events during studies (time markers)
CO2 Sensor
CO₂: 0–18% (only with Basic L Logger)

## Slide 16: Integrated Sensors
The Sensor Element and Logger are one unit and can´t be exchanged.
(only available as single sensors)

## Slide 17: TrackSense® Compact Logger
A cost-effective solution for users who do not require replaceable sensors.
Temperature Data Logger
-30 to +140 °C
Accuracy: ±0.1 °C
30,000 points
Pressure Logger
10 mBar to 6 Bar
Accuracy: ±0.25% FS
5,000 points

## Slide 18: TrackSense® Frigo Logger
Temp: -90 to +85 °C
Accuracy: ±0.1 °C
60,000 points
TSF battery for long-term use (up to 12 months)
LED indicator for activity
Ideal for: refrigerators, freezers, incubators, water baths

## Slide 19: TrackSense® Pro Mini Logger
The mini-logger was developed for processes where a small size plays an important role in avoiding thermal conduction errors. (ideal for pharmaceutical applications)
Temp: 0 to +140 °C
Accuracy: ±0.05 °C
30,000 points
Small size ideal for pharma use

## Slide 20: TrackSense® Pro Micro Logger
Temperature logger
Temp: -20 to +140 °C
Accuracy: ±0.05 °C
14,500 points
Pressure-/Temperature logger
10 mBar to 6 Bar
Accuracy: ±0.25% FS
30,000 points

## Slide 21: TrackSense® Pro LAB Logger
For temperature and humidity measurements
Including LED alarm function:
Ideal for monitoring temperature or humidity in long-term stability applications or during the validation of cleaning and disinfection systems.

## Slide 22: TrackSense® Pro Lab Logger
Temperature logger
Temp: -30 to +100 °C
Accuracy: ±0.1 °C
120,000 points
Humidity-/Temperature logger
Humidity: 0–100% RH
Accuracy: ±2% RH
30,000 points/channel

## Slide 23: Specifications Overview
Logger | dimensions (mm) | Data Storage | Battery Lifetime (h) | Temperature range (°C)
TrackSense® Pro XL | 25 x 68,8 | 120.000 | 3.000*1 | -80 bis +150
TrackSense® Pro X | 25 x 43,5 | 120.000 | 2.000*1 | -80 bis +150
TrackSense® Pro | 25 x 43,5 | 120.000 | 2.000*1 | -50 bis +150
TrackSense® Pro Basic | 25 x 43,5 | 120.000 | 2.000*1 | -30 bis +105
TrackSense® Pro Basic L | 25 x 68,8 | 120.000 | 150*2 | -30 bis +85
TrackSense® Pro Mini 2G | 20 x 12 | 30.000 | 200*3 | 0 bis +140
TrackSense® Pro Micro (TMP) | 15 x 22 | 14.500 | 75 | -20 bis +140
TrackSense® Pro Micro (PRS/TMP) | 15 x 30 | 30.000 | 50 | -20 bis +140
TrackSense® Lab | 25 x 43,5 | 60.000 | 2.000*1 | -30 bis +100
TrackSense® Pro Compact | 25 x 35 | 30.000 | 2.000*1 | -30 bis +140
TrackSense® Pro Compact X | 25 x 35 | 30.000 | 2.000*1 | -50 bis +140
TrackSense® Pro Compact UX | 25 x 60 | 60.000 | 3.000*1 | -80 bis +140
TrackSense® Frigo | 25 x 60 | 60.000 | 3.000*4 | -90 bis +85
*1 121 °C / 10 Sec. samplerate / 1 Temperature Sensor
*2 40 °C / 2 Min. samplerate / CO2 Sensor
*3 2nd Gen
*4 -80 °C / 15 Sek. Samplerate
Notes: *1 Bei 121 °C / 10 Sek. Taktrate / 1 Temperatur Sensor
*2 Bei 40 °C / 2 Min. Taktrate / CO2 Sensor
*3 2nd Gen
*4 Bei -80 °C / 15 Sek. Taktrate

## Slide 24: The most important applications
Application | TS Lab | TSP Micro | TSP Mini | TSP Basic | TSP | TSP X | TSP XL | Com-pact | Com-pact X | Com-pact UX | Frigo
Autoclave |  | X | x |  | x | x | x | x | x | x | 
Vacuum-Autoclave |  | x |  |  | x | x | x | x | x | x | 
EtO Autoclave |  |  |  | x | x | x | x |  |  |  | 
Rotations-Autoclave |  | x |  |  |  |  |  |  |  |  | 
Cleaning and disinfection device | x | x | x | x | x | x | x | x | x | x | 
Oven (over +150 °C) |  |  |  |  | x* | x* | x* |  |  |  | 
Incubator | x | x | x | x | x | x | x | x | x | x | 
Fridges | x | x | x | x | x | x | x | x | x | x | x
-40 °C Freezer |  |  |  |  | x | x | x |  | x | x | x
-80 °C Freezer |  |  |  |  |  | x | x |  |  | x | x
-90 °C Freezer |  |  |  |  |  |  |  |  |  |  | x
* Requires the use of a thermal barrier

## Slide 25: Sky System – Real-Time Data Transmission
Sky Access Point
Enables remote start/stop
Continuous process monitoring
Operating Temperature | 5 bis 50 °C
Environment | 0 bis 90 % RH, non condensing
Capacity | 1 to 4 Sky Access Points per study/process up to 64 Sky Modules (Loggers) / 128 channels
Transmission rate | 5, 10 or 60 seconds for 16 sky modules 10 or 60 seconds for 32/64 sky modules
PC-Connection | PC-connection via Ethernet or USB
Power supply | USB Link oder 12-36 VDC Supply
status indicator | LED

## Slide 26: Sky System – Real-Time Data Transmission
Sky Modul
Sky Module
Wireless communication
No data loss during transmission issues, data is stored in logger
Operating Temperature | -80 bis 140 °C
Transmission distance | Up to 15 m
Operating transmission frequency | 2.4 GHz/IEEE 802.15.4 Standard
Diameter | 25 mm
Length of the data logger with Sky module | 66,3 mm
ATEX protection class (when using Basic/Pro/X data loggers) | Ex II1G Ex ia IIC T3 Ga -60 °C ≤ Tamb ≤ 105 °C
ATEX protection class (when using XL data loggers) | Ex II1G Ex ia IIC T3 Ga -55 °C ≤ Tamb ≤ 105 °C

## Slide 27: Sky System – Real-Time Data Transmission

## Slide 28: High-Performance Lithium Batteries
Our tip:
If lithium batteries are only used in a temperature range, such as during sterilization, the lifespan can be significantly extended.
A frequent change of temperature ranges (e.g., from sterilization to freeze-drying) is not recommended by Ellab (it adversely affects the capacity)!
ISO-certified
Enhanced lifespan when used in consistent temperature ranges

## Slide 29: Use of third-party batteries may:
  Void warranty
  Cause measurement errors
  Lead to logger or sensor damage

## Slide 30: Battery Replacement
Can be performed by the user
Battery activated for 1 hour before installation
Must be confirmed in software

## Slide 31: Validation Accessories
Ellab provides the right sensor, feedthroughs, seals, and brackets for every container or product.

## Slide 32: Thermal Barrier Use for High-Temp Applications
Enables measurements up to 400 °C
Compatible with single/double rigid or flexible sensors

## Slide 33: Temperature-time profile of the thermal barriers

## Slide 34: Application Tunnel & Oven
Long tunnels make it almost impossible and very time-consuming to move thermocouples through the heating zone.
35 mm thermal barrier with 300 mm single or dual sensors (flexible)
The Challenge
The Solution
Notes: Customer: Merck & Co.

## Slide 35: Application of steam sterilization (1/2)
There are very small containers that rotate during sterilization.
Ellab Mini-Logger
Micro Logger
The Challenge
The Solution
Notes: Customer: Merck & Co.

## Slide 36: Application of steam sterilization (2/2)
Vials/Ampoules Validation
Infusion bag validation

## Slide 37: Application Sterilization
Stand-up pouch with special holder
Mini Logger

## Slide 38: Application of fermenters and SIP systems

## Slide 39: Application bottles
Distribution & Penetration temperature

## Slide 40: Summary – Key Advantages
FDA 21 CFR Part 11 compliant
-196 to +400 °C temperature range
Customizable for any process or product
Real-time data via Sky Technology
Interchangeable and integrated sensor options